## Slide 1: I3S version 1.7
Ronald Poirrier - rpoirrier@esri.com

## Slide 2
Deliver high performance 3D meshes to customers
  Upgrade I3S specs to reduce latency & bandwidth usage
  Upgrade 3D clients
  Provide tooling to content providers:
    Optimize existing content ( v1.6 -> v1.7 upgrade tool)
    I3S SDK to help with generating I3S content

## Slide 3: Design goals
Forward-compatibility with v1.6
Reduce latency due to dependent requests
Remove superfluous requests (i.e. sharedResource, featureData)
Reduce bandwidth (compression)

## Slide 4: Forward compatibility
Benefits:
“Opt-in” approach to new specs
Progressive roll-out on the platform
Transparent to end-users
Legacy
Server
Server
SLPK 1.7
Service 1.7
Service 1.7
Drawbacks:
  Increased storage size (mostly from geometry duplication, possibly DDS duplication (to avoid loss of alpha channel in WSV )
  More complex to create and edit (SDK would help here)
Clients
1.7
Clients
1.6

## Slide 5: Overview
+--3DSceneLayer.json (with added fields)
+--nodes
| +--0
| | +--3dNodeIndexDocument
| | +--features
| | +--attributes
| | | +--0
| | | +--(...)
| | +--geometries
| | | +--0
| | | +--1
| | +--shared
| | | +--sharedResource
| | +--textures
| | | +--0 (e.g. "jpeg")
| | | +--1 (e.g. "dds")
| | | +--(...)
+--nodepages
| +--0
| +--1
| +--(...)
+-- statistics
unchanged
added to specs v1.7
deprecated
Node pages meta-data:
  nodes per page, lod metric.
Texture-set definitions
  Replaces sharedResources
  Simpler definition of available compressed formats
Material definitions
  Replaces sharedResources
  glTF equivalency (metallic-roughness material model)
Mesh definitions
  replaces defaultGeometrySchema
  replaces sharedResources.
  Describes compressed geometry
Compress geometry buffer (Draco)
Paged-nodes.

## Slide 6: Performance: Paged-index example
page_id = floor( node_id / node_per_page)
node_id_in_page = modulo( node_id, node_per_page)
{
  "index": 1024,
  "lodThreshold": 50.43,
  "obb": {
    "center": [20.82,41.988,76.56],
    "halfSize": [64.93,11.4,70.315],
    "quaternion": [-0.0,0.03,-0.20569,0.9]
    },
  "children": [2025,2036],
  "meshes": [
  {
"material": {
"definition": 0,
"resource": 1000
},
  "geometry": {
  "definition": 1,
  "resource": 1000,
  "vertexCount": 14587,
  "featureCount": 1
  },
  "attribute": {
  "resource": 500
  }}]
}
This node index (page_id = 1024/64 = 16)
url: /layers/0/nodepages/16
Index of the children in the node array ( both on page 31)
url: /layers/0/nodepages/31
Index material definition for this node (see 3dSceneLayer.json)
Mat. Texture: /layers/0/nodes/1000/textures/…
Mesh definition (geometry/attribute buffers) (see 3dSceneLayer.json)
Geometry: /layers/0/nodes/1000/geometries/…
Attributes: /layers/0/nodes/500/attributes/…
Notes: Resource ID for each facilitate:
Editing
Shared resources across nodes.

## Slide 7: Performance: remove “sharedResource”
shared.material: moved to layer.materialDefinitions
shared.texture: moved to layer.textureSetDefinitions
Resources are implicitly shared (texture, attributes, geometries) using indirection ID:
  node.geometry.resource
  node.material.resource
  node.attributes.resource

## Slide 8: Performance: remove “sharedResource”
{"textureSetDefinitions": [
  {
  "formats": [
    {
    "index": 0,
    "format": "jpg"
    },{
    "index": 2,
    "format": "dds"
    },{
    "index": 4,
    "format": "ktx-etc2"
    }
  ],
  }]}
Per-node texture definition 0 with support for jpg, dxt and etc2 compression:
url: /layers/0/nodes/{resource_id}/textures/4.jpg
url: /layers/0/nodes/{resource_id}/textures/1.dds
url: /layers/0/nodes/{resource_id}/textures/2.ktx
"materialDefinitions":
{
"alphaCutoff": 0.25,
"doubleSided": true,
"atlas": false,
"pbrMetallicRoughness": {
"baseColorTexture": {
"textureSetDefinitionId": 0,
"texCoord": 0
}
}
},
Material definition:
- Physically-based rendering (pbr) metal roughness model
- Equivalency with glTF

## Slide 9: Performance: Geometry compression
Legacy geometry buffer is left unchanged, but benefits from simpler layer.geometryDefinition
Additional Draco compressed mesh resource:
  Typical saving: 40-60%
  Vertex attribute indexing may be retained
  Extended to embed FeatureID and UV_regions
  Future proof: additional vertex attributes may be added (uv[n]), multiple encoding may be supported, etc.

## Slide 10: Performance: Geometry Definition example:
"geometryBuffers": [
{
"offset": 8,
"position": {
"type": "float32",
"component": 3
},
"normal": {
"type": "float32",
"component": 3
},
"uv0": {
"type": "float32",
"component": 2
},
"color": {
"type": "uint8",
"component": 4
},
"featureId": {
"type": "uint64",
"component": 1,
"binding": "per-feature"
}
},
{
"compressedAttributes": {
"encoding": "draco",
"attributes": ["position","uv0","color","feature-index"]
}}]
Legacy mesh definition ( on index 0)
url: /layers/0/nodes/{resource_id}/geometries/0
Draco mesh definition ( on index 1)
url: /layers/0/nodes/{resource_id}/geometries/1

## Slide 11
Pro
ArcGIS 10.x
AGOL
Scene Viewer
Run Time
Apps
UC
Dev Summit
7.1
7.2
CityEngine
2019.0
100.5
2.4
10.7
Earth
1.9
CityEngine
2019.1
10.7.1
2.3
2.3.1
Earth
1.10
I3S
Specification
1.6 public spec
1.7 internal spec
Release Schedule
Jan
March
May
July
Feb
April
June
1.7 public spec
I3S SDK
spec presented

## Slide 12: Promote I3S adoption:
Comprehensive documentation generated from schema, including examples and implementation guidelines.
JSON Schema validation of all profiles and all versions starting from 1.6
Tools to convert 1.6 to 1.7 Integrated Meshes and 3D objects
I3S SDK to help create (v1.7) and read (1.6+) I3S Scene Layers

## Slide 13: SDK for I3S content
Benefits
Refined control over Scene Layer performance
Encourages I3S adoption and brings more content to the platform
Helps with compatibility issues and specs upgrades
Minimal shippable product
Closed-source SDK with C++ API (win32/64).
Self-contained, released on Esri GitHub. No ArcGIS11 dependencies.
Support for writing Integrated meshes (no LOD generation)
Support for “optimizing” SLPK from v1.6 to v1.7
Validation tool for SLPK including stats and performance warnings
{SDK}