## Slide 1: Nodes in i3s
A 100KB
B 4MB
1
NID
(1K)
FeatureData
(10K)
Geometry
(500K)
Textures
(3.6M)
Example Constraints per node: 5 MB, maximum 500 features
Notes: LoD is tied to the index structure, which is determined by loads.
All nodes have the same capacity limits.

## Slide 2: Dealing with Heavy Features
A 50KB
B 50KB
D 50KB
2
21
22
C
-> C.1
-> C.2
child
child
lodChildren
C
8MB
C.1 C.2
4MB 4MB
URL reference
ID reference
Notes: We pull down the zipper on that heavy feature.
A heavy feature is exploded in as many parts as required so that no part exceeds node capacity. Typically this is done by exploding it to geometry parts/components.

## Slide 3: Feature-based LoD
A
100KB
B
4MB
E
2MB
C
30KB
D
30KB
2
21
22
child
child
A
50KB
B
2MB
Capacity: 3 Features 5 MB
E
1MB
Source: CityGML LoD 1
Source: CityGML LoD 2
Notes: 2 separate issues:
Where do the LoDs come from?
How to manage the representation of each feature?
Having Feature-based LoD is independent of the geometry & texture aggregation!

## Slide 4: Feature-based LoD with Aggregation
A
100KB
B
4MB
E
2MB
C
50KB
D
50KB
2
21
22
AB
2MB
DE 1MB
Capacity-driven texture & geometry reduction
Capacity: 3 Features 5 MB

## Slide 5: LoD Precision
The Precision value…
  describes the maximum error relative to the node’s diameter, introduced through any processing such as LoD generalization
Calculation is based on pick the largest of the following values:
  When removing triangles, it is equal to the diameter of the circumscribing circle of the largest removed triangle.
  When removing features, it is equal to the diameter of the Minimum Bounding Sphere of that feature.
  When moving points, it should be the maximum distance that a point was moved.
2
DE
E
D
a‘
a
P = (a-a‘)/r
P = 0
At leaf level, 0 so it‘s always rendered
21
Notes: Every node has a precision value that a client can use to pick the appropriate level of detail.

## Slide 6: LoD Selection, Example
Determine screen size of Node 2 mbs: 200px
If screen size > tolerated screenspace error (10px): true
  Determine screen size of precision value: 16px
  If screen size > tolerated screenspace error: true
    Get child Node 21, start at (1). As 21 is a leaf with p = 0, it will be rendered.
  Else:
    Render Node 2
Else:
  Go up to higher level of detail
2
DE
E
D
21
a‘
a
P = 0.08
P = 0.00
Notes: The client knows about the toelrated screenspace error, e.g. 10px or 1% of the height of the screen.

## Slide 7: Index Structure
root
0
1
2
3
3-0
3-1
3-2
3-1-0
3-1-1

## Slide 8: Feature-Switching
3
3-0
3-1
3-2
3-1-0
3-1-1
1
2
3
4
5
6

## Slide 9: Node-Switching
3
3-0
3-1
3-2
3-1-0
3-1-1
1
2
3
4
5
6
1-5
5,6
5,6
2,3
Feature 6 is not represented anymore
4

## Slide 10
Bundle 0
Bundle 1
Bundle 2
Bundle n
Feature Data Doc. 0
Feature Data Doc. 1
Feature Data Doc. 2
Feature Data Doc. n
Geometry Data TypedArray 0
Node 3-3-4-1, 10 MB capacity
Texture Set 0_0
Texture Set 0_1
Geometry Data TypedArray 1
Geometry Data TypedArray 2
Texture Set 2_0
Texture Set 2_1
Geometry Data TypedArray n
Texture Set n_0
Texture Set n_1
Bundle capacity: 512KB
A Node may have any number of textures.
EXAMPLE Size: 40KB
EXAMPLE Size: 140KB
EXAMPLE Size: 250KB
EXAMPLE Size: 70KB
Contains a subset (1..*) of all features belonging to the node.
Set of 1..* Textures for LOD 0 (Full resolution).
Texture LOD 1 (Half resolution).
Texture Set 1_0
Texture Set 1_1
Shared Resources

## Slide 11: Scene Layer Package (SKP)
Archive.skp
metadata.json
/nodes/
/nodes/root/
3dNodeIndexDocument.json
features/*
geometries/*
textures/*
3dScenelayer.json
shared/*
/nodes/1-4-2-0/
3dNodeIndexDocument.json
features/*
geometries/*
textures/*
shared/*